Imagerie numérique
Examen

---
Fourier series. Explain the main principles of periodic function approximation. Explain 3 forms of Fourier series approximation (it can be interpreted as an inverse transform).
1.1
First thing we must know is that we can write cos as a function of a sin function by adding a phase shift:
We must be familiar with Euleur’s formula as well.
Which brings us to the conversion formulas.
Given any periodical function, Fourier Series tells us that we can approximate it by:
  1. a weighted sum of sine and cosine functions
[Speaker Notes: We can add a phase shift to go from sin to cos function The euleur formula is just another way of representing this formula, sin is multiplied by j, because sin represents the Im, and cos the Re part These conversion formulas will be used later The principle of periodic function is what is written in blue !]

---
1.1
Fourier series is a representation of a periodic function, based on a summation of sine and cosine functions.
Let’s assume the period is T, then we will sum up sinusoids with frequencies that are multiples of . Each sum is represented by a value k.
[Speaker Notes: We represent the kth sinusoidal function with its amplitude, frequency, and phase, because of the sin() formula, we can develop and get the formula with cos and sin, as well as the REAL coefficients ak and bk With these formulas in mind, we can introduce the following formulas : These formulas are the same, as shown by the computations previously]

---
1.1
Finally, by using the conversion formulas, we can compute a third formula from the first one:
[Speaker Notes: What we do is we apply the conversion formulas that we saw in the first slide Then we distribute ak/2 and bk/2 We replace 1/j with –j We put the terms we can in evidence, (the exponentials) -> which gives us (1/2(ak-jbk)) & the other one We define them as Fk and F-k, as the only thing that changes is the sign We change the bounds of the summation! -> Fk is complex obv]

---
Fourier series. Explain the direct and inverse Fourier series computation. Explain why for the continuous time periodic functions do we have discrete Fourier coefficients? You can use an example of periodic square signal to explain the properties of Fourier series coefficients.
1.2
The direct and inverse Fourier series computation are the formulas, we are going to use to compute the Fourier coefficients, as well as how to compute the function from these same coefficients.
The analysis, or direct Fourier is the operation we use when we have access to the periodic function and want to compute the Fourier coefficients (amplitudes and phases). These coefficients tell us how much of a particular frequency is present on the signal. The formulas are the following:
[Speaker Notes: Basically, how we change domains -]

---
1.2
The synthesis, or inverse Fourier let’s us recompute the signal from the coefficients. We do this by using the coefficients. To perform this operation, one simply must add up the sinusoids with the coefficients. The formulas are the following:
If the signal was odd, then all the coefficients are equal to 0, because cos function is even.
If the signal was even, then all the coefficients are equal to 0, because sin function is odd.
[Speaker Notes: Continuation of coefficients ?]

---
1.2
Let’s consider a simple example, the square signal.
It is an even function with period T, its amplitude is A, and pulse width Tp.
As seen before, because the function is even, = 0 for all k.
represents the average, which can be computed with:
For every other we use the formula seen before:
[Speaker Notes: Integral : because the signal is equal to 0 in [-T/2, -Tp/2] and [Tp/2, T/2], we can take these part out of integrals. Then, the signal is always equal to A, so we replace f(t) by A Then, because it is even -> it is symetric, so we can just comput from 0 to Tp/2, and multiply the result by 2.]

---
Fourier transform in continuous time and frequency. Explain the transition from periodic functions to aperiodic ones. Explain what is the main difference between the Fourier series and Fourier transform coefficients.
1.3
What we saw with FS, only works if our function is periodic, but in real world applications, functions will, most often than not, be aperiodic.
The goal is to ‘transfer’ the results we had with FS and periodic functions, into aperiodic functions. It’ll be called Fourier Transform.
We have 2 options:
  1. We can change cancel out the values of our aperiodic function, by multiplying everything outside our interval T, by 0.
  1. We can set so that the whole aperiodic function becomes a periodic function of period
[Speaker Notes: What is a periodic function ? What is a non periodic function ? We will work with option (2), and demonstrate how we compute everything]

---
1.3
We defined as inversely proportional to T, so as T grows, becomes smaller.
The ‘consequences’ of this change in can be seen in the following formula:
The following are the new DT and IT formulas:
[Speaker Notes: We start, as before, by computing Fk as before between –T/2 and T/2 We can now replace the periodc function with an aperiodic function that is in fact periodic inside the interval of integration Finally we replace the bounds of integration, from –inf to inf, since T -> inf We have (1) DIRECT TRANSFORM (2) INVERSE TRANSFORM f(t) can be complex or real, F(w) is obviously real, since we multiply by complex exponant. In the inverse transform, since we multiply by the opposite complex exponant, we get back our real function (if it was real)]

---
1.3
This leads to the following conclusion :
If f(t) is periodic, we compute FS, and are discrete coefficients.
If f(t) is aperiodic, we compute FT, and are (almost) continuous coefficients.
[Speaker Notes: VERY IMPORTANT ---- Fk ----- become continuous coefficients]

---
Fourier transform in continuous time and frequency. Explain Fourier transform as a projection onto complex exponent basis functions. Explain the corresponding properties of real and imaginary parts linking them with the properties of cosine and sine functions.
1.4
When we want to compute the DFT for a continuous signal we use the following formula:
As seen before, we can decompose this formula with Euleur’s formula:
We get the following result:
[Speaker Notes: Can recall the formulas from the previous questions The decomposition is -> distribute the integral. Real part is well represented with the cosine function and imaginary with sine function With this formula, we clearly see that it is a projection onto the cosine and sine functions]

---
1.4
Let’s represent the vector f(t) in its vector form, we can then visualize the projection onto the sine or cosine functions:
If this basis function is orthonormal, it means that we can invert, and go back to the time domain.
[Speaker Notes: The real value coeeficients are the ak or bk values, the amplitude. The basis function are just sine and cosine waves]

---
1.4
Let’s see the properties of real and imaginary parts.
Let’s start by expressing the FT of a signal, and split it in even and odd part:
Then we can distribute:
Split the integral and get:
[Speaker Notes: Any function can be split into even and odd part We can distribute and get a very large line that was suppressed here But basically, if we have two odd functions that multiplay, the result is even, and if two even functions multiply, result is even too However, if we multiply odd by even, we get odd result, and as the integral of an odd function adds to 0, by definition of odd functions, we can then suppress them from the integral. The result from the even integral, is the real part And from the odd integral is the imaginary part]

---
1.4
From the previous demonstration we get:
(1) if signal is real :
(2) if signal is real and even:
(3) if signal is real and odd:

---
Fourier transform in continuous time and frequency. Explain properties of Fourier transform under time and frequency shifts.
1.5
There are many reasons as to why we want to work in the Fourier domain instead of time domain, but before doing so, we must learn the properties, some of the properties will help doing analysis using FT, these properties usually tell us how the FT changes if the signal undergoes a certain change.
The first one is linearity:
[Speaker Notes: Les flèches expliquent bien les opérations]

---
1.5
Shifts in time:
[Speaker Notes: On the left we have time shift -> très important, la magnitude reste la même lors du shift ! -> la partie réelle et imaginaire changent, la phase aussi. Example -> we have the representation of a real valued signal. The real values are not nul, and the imaginary values are equal to 0. If we do a shift, we easily see that the imaginary values are non nul, but however, as the magnitude is the same in both examples, that is because after the shift, the real and imaginary values compensate themselves -> see formula of magnitude! -> the imaginary is non nul after shift, but real value is different as well !]

---
1.5
Shifts in frequency:
However, the difference in the signal is a complex multiplier, if our signal was real, this complex multiplier won’t make a difference.
If our signal was complex to start with, then both the magnitude and phase will change.

---
Fourier transform in continuous time and frequency. Explain properties of Fourier transform under time reversal. Explain the effects observed on slide 47, Theme 7 block 2 under phase flipping in the Fourier domain. Provide mathematical justification. Explain signal scaling in the time/spatial domain and its counterpart in the Fourier domain.
1.6
Let’s visualize time what time reversal does to our signal (real signal):
If we were to compute the FT of both those signals, we would get different results:
If the signal was real, then it’s not important, as the imaginary part is equal to 0.

---
1.6
Let’s consider this example, where we see the original signal, and then
the signal after the phase was flipped.

---
1.6
Let’s talk about signal scaling.
The thing to know, is that signals that are narrower in time, will be broader in frequency, and vice versa. Here is a visualization :
The simplest example is the delta function, a unit pulse with very small duration in time, that becomes an infinite length constant in frequency.
[Speaker Notes: Hwere we see proof And visualisation, in the same plot we see the signal as well as its frequency (spatial domain) -> in same plot to save space]

---
Signal sampling in the time/spatial domain. Explain discrete time Fourier transform. Explain the properties of spectra of discretised signals. Explain the conditions of lossless data sampling allowing signal reconstructions and provide the definition of Nyquist sampling theorem.
1.7
Sampling is to represent a given continues signal f(t), by a discrete time representation.
The hard part about sampling, is to know how many samples should we take from the continuous signal, to have the best discrete representation.
Let’s see some examples:
This process is obviously not revertible,
because of all the points that aren’t sampled.
However, we’ll later see that we can recover
the continuous signal.
[Speaker Notes: In this examples we can see how gradually increasing the number of samples changes the fonction we have as a result. We go from under sampling to over sampling The problem is not HOW MANY samples, but WHERE to sample]

---
1.7
To sample a signal, we will multiply it by an impulse train, which is a train of delta functions.
By the properties seen for the FT, we know that if we multiply in the time domain, the equivalent operation in Fourier domain is the convolution.
Let’s consider this signal in the Fourier domain:
  - It is band limited between [-W, W]
  - When convoluted by the Fs of an impulse train it ‘copies’ itself at a specific rate
  - This rate depends on Ts
Fs
[Speaker Notes: We can see in the example the difference that Ws size will make. On the left, a signal Middle -> sampling at a greater rate than Nyquist rate Right -> samnpling at right rate, and at less than Nyquist rate]

---
1.7
Let’s now talk about Nyquist sampling theorem, or sampling theorem.
This theorem concerns ‘bandlimited’ signals, f(t), that are equal to 0 for all frequencies except for a band limited part.
limit
This theorem states that there is a sampling frequency, from which it will be possible to reconstruct the unique f(t) .
What we saw before, are the effects of sampling at different rates:
  - we can over sample.
  - Sample at the Nyquist rate
  - Under sample -> results in Aliasing
The goal is to sample at the right rate, so that we don’t use up our memory
or that we aren’t affected by aliasing.

---
Signal sampling in the time/spatial domain. Explain the principles of ideal signal reconstruction. Explain an ideal low pass filer based reconstruction.
1.8
Sampling